## Slide 1
UAM Hexacopter
Multidisciplinary Design Optimization Framework
FrameworkCpp · A C++ MDO System for eVTOL Hexacopter Design Optimization
Pagmo2 · CMA-ES / NSGA-II
ACS · Structural · Powertrain
16 design variables
18 hard constraints
Multidisciplinary Design Optimization of Aerospace Systems · 2026

## Slide 2
Project Overview
02
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
①
Study Object
UAM (Urban Air Mobility) hexacopter
— 6-motor asymmetric hexacopter architecture
— Designed around an eVTOL operating mission
②
Objective
A single MDO framework that simultaneously couples
structure · propulsion · ACS · powertrain · battery
— supports both single- and multi-objective search
③
Key Contribution
High-performance C++ evaluation engine
+ Pagmo2 (CMA-ES / NSGA-II) integration
+ real-time 3D visualization (ImGui / Vulkan)
Framework at a Glance
5
analysis disciplines
structure · ACS · powertrain · battery · packaging
16
active design variables
geometry 4 + structure 2 + battery 1 + positions 9
18
hard constraints
geometry · packaging · ACS · structural · battery
2
optimization algorithms
SOO (CMA-ES) + MOO (NSGA-II)

## Slide 3
Optimization Design Variables (16 active)
03
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Geometry
Lx
default 2.65 m · range [2.0 – 5.0]
Lyi
default 2.65 m · range [2.0 – 5.0]
Lyo
default 5.50 m · range [2.5 – 9.0]
T_max
default 12000 N · range [8k – 20k]
Structure & Energy
arm_outer_radius
default 0.08 m · [0.02 – 0.15]
arm_wall_thickness
default 0.005 m · [0.001 – 0.020]
m_bat
default 400 kg · range [100 – 1000]
Passenger Position
pax_x
0.00 m · range [-0.25, +0.25]
pax_y
0.00 m · range [-0.42, +0.42]
pax_z
-0.10 m · range [-0.50, +0.40]
Cargo Position
cargo_x
0.00 m · range [-0.50, +0.50]
cargo_y
0.00 m · range [-0.45, +0.45]
cargo_z
0.75 m · range [0.30, 1.00]
Battery Position
bat_x
0.00 m · range [-0.50, +0.50]
bat_y
0.00 m · range [-0.55, +0.55]
bat_z
-0.90 m · range [-1.00, +0.85]
Variable handling
• All 16 variables normalized to [0,1]; DesignVectorMapper → physical units.
• pax / cargo / battery are element-owned body-frame placement variables (each element encodes them in its local_pose_) — this is why packaging constraints and the 3D viewer matter.
★ Fixed (inactive) parameters: cT = 0.03, d_prop = 0.40 m, m_pax = 600 kg, m_cargo = 200 kg, m_instrument = 50 kg — mission requirements, not optimized.

## Slide 4
Objective Functions & Hard Constraints
04
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Objectives (weighted-sum SOO / Pareto MOO)
mass
w = 0.20
total vehicle mass (normalized)
power
w = 0.20
hover power proxy
fault_thrust
w = 0.25
single-motor-fault thrust-margin penalty
fault_alloc
w = 0.25
control-allocation degradation ratio
hover_nom
w = 0.10
nominal hover thrust utilization
cabin_space_penalty
w = 0.10
cabin packing / space penalty
acs_margin_penalty
w = 0.10
ACS directional-margin penalty (≥0 healthy)
structural · packaging · structural_safety carry weight 0 → analysis-only metrics.
Hard Constraints (large penalty on violation)
GEO
parameter_bounds ≤ 0
GEO
minimum_geometry_margin ≥ 0
GEO
rotor_clearance ≥ 0
PACK
payload / battery / occupant in cabin
PACK
battery-payload & component non-overlap
CG
cg_envelope |x|≤0.40, |y|≤0.25 m
ACS
failed_hover_gamma ≥ 1.5
ACS
fault_allocation_ratio ≥ 0.05
ACS
all_faults_hover_feasible ≥ 0
ACS
fault_directional_margin ≥ 0
STR
arm_yield_failure ≥ 1.5
STR
arm_tip_deflection ≤ 0.10 m
STR
arm_tip_rotation ≤ 0.10 rad
BAT
battery_energy_reserve ≥ 0
BAT
battery_crate_limit ≤ 5 /h
18 architecture-level hard constraints total (packaging row groups 5 sub-checks).

## Slide 5
Multidisciplinary Evaluation Pipeline (Stage1Evaluator)
05
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Step 01
Vehicle Scaling Model
Mass · CG · inertia · thrust
battery-mass feedback included
Step 02
ACS Analyzer
Nominal + 6 fault hover trims (LP)
margins · retention · feasibility
Step 03
Structural Network
Multi-member network, 8 load cases
von Mises SF · tip deflection
Step 04
Powertrain Evaluator
Actuator-disk power model
per-motor electrical power [W]
Step 05
Battery Evaluator
Energy budget · reserve fraction
C-rate (mission-aware)
Step 06
Constraints + Objective
18 hard-constraint checks
weighted-sum aggregation
Call order matters: ACS runs before structural (fault trims become load cases); packaging runs after structural.
▶ EvaluationResult = PhysicalModel + AcsResult + PowertrainResult + BatteryResult + constraint_results + combined_objective

## Slide 6
Phase 1 — Structural Analysis & ACS
06
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Structural Network Analyzer
▸ Hollow circular tube cross-section per arm
▸ Outer radius r₀, wall t → second moment I
▸ Max bending load = motor thrust × arm length
▸ 8 load cases: max-thrust, hover, fault_0–5
▸ Safety factor SF = σ_yield / σ_bending ≥ 1.5
▸ Euler–Bernoulli tip deflection & rotation
Attainable Control Set Analyzer
▸ Allocation matrix B ∈ ℝ⁴ˣ⁶ (thrust·roll·pitch·yaw)
▸ LP hover trim: nominal + 6 single-motor faults
▸ Directional margin m(d) = h_U(d) − dᵀ·u_req
▸ PFWAR — probability-weighted ACS retention
▸ WCFR — worst-case fault retention
▸ FII — fault isotropy index (FII < 1 is ideal)
ACS correctness invariant
margin(d, u) = h_U(d) − dᵀ·u ≥ 0 feasible h_U(d) = Σⱼ max(0, dᵀ·bⱼ)·f_maxⱼ (never use the sign-flipped form).
ACS output files (--plot-acs)
acs_fig5_hover_poly.svg
— hover moment polygon
acs_fig6_margins.svg
— per-direction margin bars
acs_retention.svg
— per-motor ACS retention
acs_vertices.csv
— 4D vertex cloud

## Slide 7
Phase 2 — Powertrain & Battery Energy Model
07
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Powertrain (PowertrainEvaluator)
Effective disk radius
r_eff = max_arm_length / 2
Electrical power (rotor i)
Pᵢ = Tᵢ^1.5 / (η_tot · √(2ρ·A_eff))
Total nominal power
P_nom = Σ Pᵢ (nominal hover trim)
Total fault power
P_fault = Σ Pᵢ (worst fault trim)
η_tot = FoM·η_motor·η_esc = 0.65·0.85·0.95. d_prop drives yaw-torque scaling only.
Battery (BatteryEvaluator)
Available energy
E_avail = η_pack · DoD · m_bat · e_spec
Mission energy demand
E_req = P_nom·t_nom + P_fault·t_emg
Energy reserve
reserve = (E_avail − E_req)/E_avail ≥ 0
C-rate
c_rate = P_peak / E_avail ≤ 5.0 /h
e_spec = 250 Wh/kg (NMC811) · DoD = 0.85 · η_pack = 0.95 · t_nom = 30 min · t_emg = 1 min
Battery-mass feedback loop
m_bat ↑ → total mass ↑ → hover thrust ↑ → power ↑ → energy demand ↑ → battery constraints re-checked
Below the minimum viable battery mass the energy reserve goes negative — the optimizer finds the nonlinear balance point.

## Slide 8
Optimization — SOO / MOO and the Search Loop
08
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
SOO — Single-Objective (SooRunner)
Algorithm
CMA-ES (Pagmo2)
Population
24 (default)
Generations
40 (default)
Search space
normalized [0,1]¹⁶
Feasibility
all hard constraints + ACS LP
Output
baseline / best_raw / best_feasible
Penalty strategy:
infeasible → 1e6 + Σ(weightᵢ·violationᵢ) + 1e4
feasible → combined_objective (weighted sum)
MOO — Multi-Objective (MooRunner)
Algorithm
NSGA-II (Pagmo2)
Population
48 (default)
Generations
60 (default)
Objectives
mass, power, fault_alloc
Output
Pareto front (feasible subset)
Knee analysis
ParetoAnalyzer (knee point)
Trade-off surface (3 objectives):
min mass ←→ min power ←→ max fault tolerance
designer selects the operating point directly
x̂ ∈ [0,1]¹⁶
→
DesignVectorMapper
→
HexacopterArchitecture
→
Stage1Evaluator
→
Pagmo fitness
→
next generation
Iterative loop: search in normalized space → map to physical units → evaluate all disciplines → feed fitness back.

## Slide 9
C++ Code Architecture (FrameworkCpp)
09
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Directory layout
FrameworkCpp/
├─ app/ (main.cpp · CLI modes)
├─ include/ + src/
│ ├─ core/ Architecture · Elements
│ ├─ physics/ Structural · ACS · Power · Battery
│ ├─ evaluation/ Stage1Evaluator
│ ├─ optimization/ SOO · MOO · Pagmo
│ ├─ analysis/ CSV · JSON · Pareto · ACS plot
│ ├─ mission/ MissionProfile · Evaluator
│ └─ calibration/ Calibrator (Nelder–Mead)
├─ visualization/ ImGui / Vulkan 3D viewer
└─ docs/ CODEBASE.md · Action.md …
Core classes
HexacopterArchitecture
root: parameter · element · constraint registries
DesignParameter
design variable (value · bounds · norm · id)
Stage1Evaluator
runs the 6-step multidisciplinary pipeline
PagmoProblemAdapter
Pagmo2 adapter (shared by SOO / MOO)
SooRunner / MooRunner
CMA-ES / NSGA-II execution wrappers
ConstraintRegistry
hard-constraint evaluation + penalties
CsvExporter
results to CSV / JSON in physical units
AcsPlotter
SVG ACS visualization (no dependencies)
ArchitectureViewerApp
ImGui / Vulkan real-time 3D viewer

## Slide 10
How to Run & Output Artifacts
10
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
CLI commands
# baseline design evaluation
FrameworkCpp.exe eval
# single-objective optimization
FrameworkCpp.exe soo --soo-pop 24 --soo-gen 40
# multi-objective optimization
FrameworkCpp.exe moo --moo-pop 48 --moo-gen 60
# full SOO + MOO comparison
FrameworkCpp.exe compare --output-dir ./out
# SOO with live 3D visualization
FrameworkCpp.exe soo --visualize
# mission / calibration subsystems
FrameworkCpp.exe mission data\...json
Output files
comparison.csv
baseline vs optimum comparison
soo_parameters.csv
SOO optimal variables (physical units)
pareto_front.csv
Pareto objectives + safety factors
soo_run.json
full SOO result (with physical model)
moo_run.json
MOO result (Pareto population)
acs/*.svg
ACS margin & retention charts
Real-time 3D visualization (ArchitectureViewerApp — ImGui + Vulkan)
• live arm / motor / rotor / payload rendering
• updates as the optimization progresses
• loads SOO/MOO results from JSON
• left panel: per-element mass & position

## Slide 11
Post-Optimization Analysis & Interpretation
11
Multidisciplinary Design Optimization of Aerospace Systems · FrameworkCpp · 2026
Each run tracks raw-best and feasible-best separately, then exports artifacts for the designer to interpret the trade space.
SOO outcome — three tracked solutions
baseline
default design vector (reference point)
best_raw
lowest objective ignoring feasibility
best_feasible
lowest objective with all 18 constraints met
MOO outcome — Pareto trade-off
• Feasible Pareto subset — non-dominated designs that satisfy every hard constraint.
• Knee-point selection via ParetoAnalyzer — best mass / power / fault-tolerance compromise.
• Designer picks the operating point along the front directly.
Post-analysis interpretation flow
ACS SVGs
directional margins,
fault retention
→
comparison.csv
baseline vs optimum,
side by side
→
*_parameters.csv
winning design vector
in physical units
→
soo/moo_run.json
full result +
physical model
→
3D viewer replay
load JSON, inspect
placement & masses
Generate everything at once: FrameworkCpp.exe compare --output-dir ./out (runs SOO + MOO and writes all artifacts).

## Slide 12
Conclusion & Future Work
✓
C++ high-performance MDO framework — 5 coupled disciplines (structure · ACS · propulsion · battery · packaging)
✓
16 design variables, 18 hard constraints → Pagmo2 SOO (CMA-ES) + MOO (NSGA-II)
✓
Phase 2: battery energy / C-rate constraints and powertrain model integrated
✓
3-DOF placement of passenger · cargo · battery with AABB cabin-packaging constraints
✓
ImGui / Vulkan real-time 3D viewer + automatic ACS SVG plots
✓
Mission and calibration subsystems (multi-segment energy, flight-log parameter ID)
Future work
→ higher-fidelity CFD / FEM coupling
→ range and noise objectives
→ flight-data-driven model calibration
→ multi-mission (cruise + hover) optimization